ME 360: Fundamentals of Signal Processing, 
Instrumentation, and Control

Experiment No. 4

Modeling and Identification of an Electric Motor using Step Response and Frequency Response Methods

Data Sheet

# Steady-State Gain (10 PTS)

| VDAC [V] | VDMM [V] | K = VDMM / VDAC [V/V] |
| --- | --- | --- |
| 3 |  |  |
| 4 |  |  |
| 5 |  |  |
| 6 |  |  |

### Observations:

# Step Response (20 PTS)

|  | Data |
| --- | --- |
|  | Vin (t ≥ 0) | 4 V |
|  | Vout (∞) |  |
|  | K = Vout (∞) / Vin (t ≥ 0) |  |
| Time at 63.2 % of Maximum Change | 63.2 |  |
| Iterative Fit of Observed Response Data | Kfit |  |
|  | fit |  |

### Observations:

# Discuss possible inaccuracies using the 63.2% rule to find K and .  Using the iterative fit method to find K and     (5 pts)

# Frequency Response (30 Pts)

| Method | Data |
| --- | --- |
| Manual Sine Sweep | f [Hz] | Vp-p, out [V] | G(f) [V/V] | tdelay [s] | (f) [°] |
| Voffset [V] |  | 0.2 |  |  |  |  |
| Vp-p, in [V] |  | 0.4 |  |  |  |  |
| Manual Sweep Calculations | 0.8 |  |  |  |  |
| K [V/V] |  | 1.6 |  |  |  |  |
| Break Freq. fb -3 dB [Hz] |  | 3.2 |  |  |  |  |
| Break Freq. fb, 45º [Hz] |  | 6.4 |  |  |  |  |
|  -3 dB [s] |  | 8.0 |  |  |  |  |
|  45º [s] |  | 10.0 |  |  |  |  |

### Observations:

# Frequency Response of Beam-mass System (5 pts)

| Results for Sine-swept Method for Beam System |
| --- |
| Parameter | measured | calculated | units |
| Primary Natural Frequency fnb |  | 21.5 | Hz |
| Gain at Primary Natural Frequency G(fnb) |  |  | dB |
| Secondary Natural Frequency fnc |  |  | Hz |
| Gain at Secondary Natural Frequency G(fnc) |  |  | dB |

What is the source of each of the primary and secondary peaks in frequency response of the beam-mass system?